## Slide 1: Bird Strike Risk Assessment Methods & Tools
Civil Air Patrol
One Civil Air Patrol, excelling in service to our nation and our members!

## Slide 2: Bird Strike Hazard
Now a required factor for airplane pre-flight risk assessment
Use the best available data to assess the risk
  Bird Watch Condition (BWC)
  Avian Hazard Advisory System (AHAS)
  Chart Supplement
  Pilot Reports (PIREPS)

## Slide 3: Bird Watch Conditions (BWC)
SEVERE
  Bird activity on or immediately above the active runway or other specific location representing high potential for strikes. Supervisors and aircrews must thoroughly evaluate mission need before conducting operations in areas under this condition.
MODERATE
  Bird activity near the active runway or other specific location representing increased potential for strikes. BWC moderate requires increased vigilance by all agencies and supervisors, and caution by aircrews.
LOW
  Bird activity on and around the airfield representing low potential for strikes.
A common element of Airfield Bird/Wildlife Countermeasure Programs. BWC is set by Airfield Operations based on numerous inputs, then relayed to pilots via ATIS and tower/approach controllers. Use where and when available.

## Slide 4: Avian Hazard Advisory System
Uses NEXRAD weather radars to detect birds and measure mass
Removes weather
Near real-time presentation of bird activity in an area

## Slide 5: United States AHAS Website
Provides a means of accessing multiple data sources and models (AHAS, SOAR, BAM)
Primary focus is on providing easy access to information regarding military airfields, operating areas, and routes
ICAO option can be used to enable selection of airfield ID; however airfields are limited
BWC is preferred over AHAS for on-airfield operations
Use when BWC is not available or when doing route surveys
www.usahas.com
2.) Select airfield ID, month, date, and time (Z)
3.) Select presentation format
4.) Copy AHAS risk descriptor
1.) Select ICAO

## Slide 6: Chart Supplement
Airport remarks
Provides basic information regarding bird and wildlife hazards
  Types
  Locations
  Months of the year
  Peak activity times
May provide a contact who can provide BWC information

## Slide 7: Pilot Reports (PIREPS)
Reports from returning pilots provide useful information; however, it may not always be timely – adjust your risk assessment, when able, and your mitigation plan as required.
In many cases, your personal knowledge of the local area will be the best available information; however, complacency due to familiarity must be avoided.

## Slide 8: Kevin Conyers Chief, Stan/Eval kconyers2@capnhq.gov dov@capnhq.gov
Questions?
One Civil Air Patrol, excelling in service to our nation and our members!